## Slide 1: MAGICAL 1.0: An Open-Source Fully-Automated AMS Layout Synthesis Framework Verified With a 40-nm 1GS/s ΔΣ ADC
Hao Chen*, Mingjie Liu*, Xiyuan Tang*, Keren Zhu*, Abhishek Mukherjee, Nan Sun, and David Z. Pan (*: Equal contribution)
The University of Texas at Austin

## Slide 2: MAGICAL: MAchine Generated IC Analog Layout

## Slide 3: MAGICAL 1.0: Hierarchical Framework

## Slide 4: MAGICAL 1.0: Constraint Generation
Pattern detection for building block symmetry [Xu+, ICCAD'19]
Graph similarity for system symmetry constraint [Liu+, ASPDAC'20]
Customizable signal-flow constraints
Building block symmetry
Symmetry nets
System-level constraints

## Slide 5: MAGICAL 1.0: Placer
Nonlinear programming-based global placement
Linear programming-based detailed placement
Using system signal flow to guide placement for mixed-signal placement
[Zhu+, ICCAD'20]

## Slide 6: MAGICAL 1.0: Placer
Consider regularity of system signal flow in placement
Improved numerical optimization kernel
Better post-layout simulation performance and placement metrics

## Slide 7: MAGICAL 1.0: Router
Grid-based routing kernel w/ DRC handling
New symmetry routing patterns
Special power/ground routing
[Chen+, ICCAD'20]

## Slide 8: MAGICAL 1.0: Router
Multiple vias and various wire widths for voltage drop consideration
Symmetry constraint allocation
  Maximize the overall potential routing symmetry (Weighted graph matching)
Pin access assignment
Access point
(source)
Pin access assignment
Gate
Drain
Source
Access point
(gate)
Access point
(drain)
Invalid access
point

## Slide 9: Simulation in the Loop
Simulation-in-loop: use simulation results on building block level circuits as the feedback to the MAGICAL P&R
Intelligent performance prediction will reduce #simulations
[Liu+, DAC'20]

## Slide 10: MAGICAL 1.0: 3rd-order CTDSM Demo
1GS/s 3rd-order high-performance continuous time ΔΣ modulator
State-of-the-art performance, originally published in IEEE SSC-L'20
Include various sub-block types
Notes:   Three integrators: One passive, two active
  Two FIR-based feedback DACs
  One comparator
  Digital logic

## Slide 11: MAGICAL 1.0: 3rd-order CTDSM Demo
*For demo purpose, simulation in the loop not included.

## Slide 12
After ~90 seconds….
Core area: 22,000 um2
Tape-out with manually designed peripherals (buffer, driver, PADs)
ADC Core
MAGICAL 1.0: Fully Synthesized ADC Core

## Slide 13: MAGICAL 1.0: Measurement
CTDSM ADC chip under TSMC40 technology
Chip micrograph of the synthesized CTDSM
PCB board

## Slide 14: MAGICAL 1.0: Measurement
Fs: 1GHz
BW: 5MHz
SNDR: 67.4dB
SFDR: 80.8dB

## Slide 15: MAGICAL 1.0: Measurement
Stable performance across 8 samples.

## Slide 16: MAGICAL 1.0: Measurement
DR: 68.5dB

## Slide 17: Comparison with SOTA CTDSM ADCs
Only require signal flow information
Comparable layout with manual design [SSCL ’20 Mukherjee]
MAGICAL 1.0
Manual

## Slide 18: Comparison with SOTA CTDSM ADCs
Fully-synthesized layout
 | JSSC-16 Weng | SSCL-20 Mukherjee1 | CICC-19 Li | This work1
Architecture | CTΔΣM | CTΔΣM | VCO-CTΔΣM | CTΔΣM
Layout synthesized | ✖ | ✖ | ✔ | ✔
Universal synthesis framework | N/A | N/A | ✖ | ✔
Hierarchical flow | N/A | N/A | ✖ | ✔
Constraint generation | N/A | N/A | ✖ | ✔
1: same schematic
Notes: MAGICAL 1.0 layout compares well with manual layout (SSCL'20) in terms of power, performance, and area (runtime O(min) vs. O(month)

## Slide 19: Comparison with SOTA CTDSM ADCs
Comparable results with other SOTA CTDSM ADCs
 | JSSC-16 Weng | SSCL-20 Mukherjee1 | CICC-19 Li | This work1
Architecture | CTΔΣM | CTΔΣM | VCO-CTΔΣM | CTΔΣM
Order | 4th | 3rd | 1st | 3rd
Area [mm2] | 0.1 | 0.034 | 0.01 | 0.033
Fs [MHz] | 320 | 1024 | 600 | 1024
Power [mW] | 4.2 | 0.79 | 1.08 | 0.77
BW [MHz] | 10 | 5 | 4 | 5
SNDR [dB] | 74.4 | 65.6 | 68.8 | 67.4
FoMw [fJ/c-s] | 49.3 | 51 | 60 | 40.2
FoMs [dB] | 174.5 | 163.6 | 164.3 | 165.5

## Slide 20: MAGICAL 1.0: Other Circuits
2nd-Order CTDSM
Inverter-Based Feed-Forward OTA
Comparator

## Slide 21: MAGICAL 1.0: Public Release
Open-sourced MAGICAL 1.0 (under BSD-3 license), https://github.com/magical-eda/MAGICAL with key updates:
  Push-button, no-human-in-the-loop (can take user constraints too)
  End-to-end analog layout generation from netlist to GDSII
  New placement and routing engines
  DRC clean, LVS clean
Real-world circuit examples (PDK-stripped)
  https://github.com/magical-eda/MAGICAL-CIRCUITS
Open-sourced UT-AnLay dataset and ML model for analog post-layout performance prediction https://github.com/magical-eda/UT-AnLay

## Slide 22: Acknowledgements
The authors thank DARPA for supporting this project and TSMC for university shuttle program.
Thank you!
Q & A